## Slide 1
SCENTINEL
An AI-Powered Personal Smell Assistant for Anosmia Patients
Voice-guided safety alerts and cooking assistance for the millions who live without a sense of smell
HACKACE 2026 · DOMAIN 1: OPEN CHALLENGE SOLUTIONS

## Slide 2
The Problem
Losing smell removes a safety sense most people never think about
2.5M+
Americans live with anosmia — and far more globally
3
Everyday danger signals missed: gas leaks, smoke, spoiled food
0
Consumer devices built for smell-loss safety today
“
Sarah couldn’t smell the gas leak in her kitchen for six hours. Her carbon monoxide detector never triggered because the leak was propane, not smoke — but her nose, if she’d had one, would have caught it in seconds.
SCENTINEL · AI Smell Assistant for Anosmia
2

## Slide 3
Existing Solutions vs. Scentinel
Smoke detectors and air-quality monitors already exist — but none of them are built for anosmia
Smoke & CO Detectors
Catch fire and CO only — miss gas leaks and spoiled food entirely
Generic Air-Quality Monitors
Show a number on a screen — no explanation, no voice, no alerting
Nothing Built for Anosmia
No consumer product today is designed around smell loss specifically
VS
Detects smoke/CO only → Scentinel detects gas, smoke, AND food spoilage
Shows a number on a screen → Scentinel speaks a plain-language alert out loud
One-size-fits-all threshold → Scentinel learns YOUR household’s own baseline
No design for anosmia at all → Purpose-built for anosmia: safety + cooking, in one device
SCENTINEL · AI Smell Assistant for Anosmia
3

## Slide 4
The Solution
A sensor pod + AI backend that speaks smell out loud
Safety Net
Detects gas leaks, smoke, and combustible fumes in real time and raises an urgent voice + light alert.
Cooking Assistance
Tells you when food smells “off” — spoiled dairy, burning food, gone-bad leftovers — before you taste it.
Voice Assistant
Ask “is my kitchen safe?” or “does this smell fine?” and get a spoken, plain-language answer.
Sensory substitution — the same principle behind vision-to-sound aids for blind users — applied to smell.
SCENTINEL · AI Smell Assistant for Anosmia
4

## Slide 5
How It Works
Sensor → classify → reason → speak
1
Sense
MQ-2 / MQ-135 / BME680 gas + VOC sensors on ESP32 read air continuously
→
2
Classify
Rule-based thresholds tag readings: smoke, gas, spoilage, or normal
→
3
Reason
LLM turns sensor data + context into a plain-language explanation
→
4
Speak & Alert
Voice assistant speaks the message; light/haptic alert fires locally
Backend: ESP32 (WiFi) → FastAPI → SQLite log → LLM API for language generation → Web Speech API (TTS) → React dashboard
SCENTINEL · AI Smell Assistant for Anosmia
5

## Slide 6
What Makes It Novel
Not “a gas sensor with an app” — an AI layer that reasons and personalizes
Personalized baselines
Learns what YOUR fridge, YOUR stove, YOUR kitchen normally smell like — not generic thresholds
Category-aware, not binary
Classifies smoke vs. gas vs. spoilage vs. normal instead of a single “danger” beep
Natural-language reasoning
LLM explains WHY an alert fired and what to check, not just that a threshold was crossed
Dual-purpose device
One low-cost device covers both emergency safety AND everyday cooking assistance
SCENTINEL · AI Smell Assistant for Anosmia
6

## Slide 7
Hardware & Software Stack
~$30–$45 in parts, no custom ML training required
HARDWARE
ESP32 Dev Board WiFi + BLE compute core
MQ-2 Gas Sensor LPG, propane, smoke detection
MQ-135 / BME680 Air quality, VOCs, ammonia
DHT22 Temperature + humidity context
Buzzer + RGB LED Local physical alert
SOFTWARE
Firmware Arduino / PlatformIO — reads sensors, posts over WiFi
Backend FastAPI + SQLite — receives data, runs classifier
AI Layer Rule-based classifier + LLM for language generation
Voice Web Speech API for speech-to-text / text-to-speech
Frontend React dashboard — live sensor status, alert log
Build timeline: hardware bring-up (0–8h) → backend + classifier (8–14h) → frontend + voice (14–20h) → integration & demo polish (20–30h)
SCENTINEL · AI Smell Assistant for Anosmia
7

## Slide 8
Live Demo Scenarios
Two real triggers, physical hardware, spoken response
Scenario A — Safety Net
1
Hold a lit lighter near the MQ-2 sensor
2
Dashboard flips to “DANGER” in real time
3
Assistant speaks: “Gas or smoke detected near your stove — please check immediately”
Scenario B — Cooking Assistance
1
Place a vinegar-soaked cotton ball near the MQ-135 sensor
2
User asks aloud: “Does this smell fine?”
3
Assistant replies: “This smells off — similar to spoiled dairy, I’d avoid it”
SCENTINEL · AI Smell Assistant for Anosmia
8

## Slide 9
Model Simulation Results
SVM classifier on a 5-class odor dataset (WEKA, 500 instances, 5 sensor features)
96.6%
Accuracy
483/500 correctly classified
96.7%
Weighted Precision
across all 5 odor classes
0.318
Root Mean Squared Error
on stratified 10-fold CV
Class | Precision | Recall | F-Measure
Gas Leak | 0.905 | 0.950 | 0.927
Smoke | 0.947 | 0.900 | 0.923
Coffee | 0.980 | 1.000 | 0.990
Perfume | 1.000 | 0.980 | 0.990
Spoiled Food | 1.000 | 1.000 | 1.000
Dataset
odor_dataset_500 — 500 instances, 5 sensor features (MQ2, MQ135, MQ136, VOC) across 5 classes: Gas Leak, Smoke, Coffee, Perfume, Spoiled Food. Trained with SMO (SVM) in WEKA, stratified 10-fold cross-validation.
SCENTINEL · AI Smell Assistant for Anosmia
9

## Slide 10
SDG Alignment
Built toward the UN Sustainable Development Goals
SDG
3
Good Health & Well-Being
Prevents harm from undetected gas leaks, smoke, and spoiled food; supports safe, independent living
SDG
9
Industry, Innovation & Infrastructure
Applies low-cost IoT sensing and AI reasoning to build new assistive infrastructure
SDG
10
Reduced Inequalities
Closes an accessibility gap with no mainstream consumer solution today
SCENTINEL · AI Smell Assistant for Anosmia
10

## Slide 11
Impact & Roadmap
From weekend prototype to a real assistive device
Who this helps
Post-viral / COVID-related anosmia patients
Congenital anosmia (born without smell)
Elderly users with age-related smell loss
Neurological patients (Parkinson’s, head trauma)
Roadmap after the hackathon
v1
Wearable enclosure + longer battery life
v2
Trained classifier replacing rule thresholds
v3
Smart-home integration (lights, notifications)
v4
Clinical pilot with anosmia support groups
SCENTINEL · AI Smell Assistant for Anosmia
11

## Slide 12
Smell is a safety sense.
Scentinel gives it back — one alert, one spoken sentence at a time.
Thank you — questions welcome